## Slide 1
The Best of Both Worlds – Combining
the QNX Hypervisor for Safety and
Virtualized Android using the
Google ‘trout’ Configuration
Randy Martin Senior Product Manager
Notes: Jw notes
-- Inconsistency between this slide and slide 11 (7 of 7 tier 1s while slide 11 says 7/8 tier 1s)

## Slide 2: Agenda
2
Trends
Hypervisor designs: Digital cockpit, rear seat, high-performance compute
Digital cockpit demonstration (Android ‘trout’ configuration)
Futures

## Slide 3: Trends in Virtualization
3
THE CLOUD
ARM Virtual Hardware, Intel virtual environments
Developers expect to easily migrate from cloud development to embedded target
CHIP VENDORS ARE ACTIVE
ARMv9, Virtualization Host Extensions (VHE)
Next generation Intel
More cores per SoC
STANDARDS, SUCH AS VIRTIO 1.2 REMAIN STRONG AND ACTIVE
More virtual device interfaces being created for Android/Linux/any OS
SoC and hypervisor vendors are providing both custom virtual solutions and standards-based solutions, and sometimes a mix of both
Google is active in virtualization of Android (Android 12, 13)
Virtual devices then migrate to Linux common kernel as well

## Slide 4: Hypervisor Designs
4
Service OS in hypervisor host
Service OS in virtual machine
SERVICE OS CONTAINS THE SOFTWARE THAT SUPPORTS THE GUEST:
Shared devices, such as disks, networking, graphics, audio
System monitoring, failover

## Slide 5: Service OS in a Virtual Machine
Hypervisor
Driver support
(pass-through)
Guest drivers virtual
Service OS / Domain0
Proprietary
sharing
Guest OS
= virtual machine
5
Selective pass-through to hardware

## Slide 6: Service OS in Hypervisor Host
6
Hypervisor
Guest drivers virtual
Proprietary
sharing
Guest OS
Selective pass-through to hardware
= virtual machine
Driver support
Sharing support

## Slide 7: QNX® Hypervisor Microkernel Design
vcpu = virtual CPU
Hypervisor host
System RAM
Private secure interface
QNX Hypervisor microkernel
User Process A
Driver Process B
Create/destroy
Command/control
7
Guest OS running in a virtual machine
vcpu0
vcpu1
IPC
Scheduling
Memory allocation
QVM
Virtualization extensions
‘QVM’ VIRTUAL MACHINE MANAGER
Separate from the microkernel
Competes with other host processes for CPU time and resources based on priority
Can be given dedicated cores or share
Safety certified
One QVM per guest
A QVM may be destroyed and restarted without rebooting
If QVM dies, the rest of the system continues operating

## Slide 8
8
© 2022 BlackBerry Limited. All Rights Reserved.
Virtualization of Android

## Slide 9: Relaxation Break
https://youtu.be/ULxMbnfbKUw used with permission
9
CANADA WARBLER
Small, like a microkernel!
10 grams, 8 cm tall
Migrates over 5000 km

## Slide 10: Google and Android® Virtualization: Many Animals to Remember
WARBLER
GULL
10
CUTTLEFISH
Virtual Android device
More advanced than Android Emulator
TROUT
Android Automotive OS built from Cuttlefish
BIRD VARIANTS
Hardware and OS specific implementations of trout

## Slide 11: QNX Integration Goals for trout Configuration
11
PROVIDE UNBOUNDED USER EXPERIENCE
Android environment and non-Android environment blend together seamlessly
Designer freedom
MEET KEY REQUIREMENTS
Functional safety, mission-critical cluster
Performance, boot times, audio latency
SUPPORT LATEST ANDROID VERSIONS, MIDDLEWARE AND EXTENSIONS
No kernel modifications, support for Vulkan drawing APIs, GfxStreams, USB sharing etc.

## Slide 12: Digital cockpit: No guests running yet
IVI
Hypervisor-enabled QNX microkernel (safety-certified)
Cluster display
Vehicle data
CRITICAL IVI SOFTWARE
Cameras
Video streaming
Vehicle HAL
Graphics
Audio
System wide audio management
Touch events
Vehicle data
Audio
USB
Network
CRITICAL CLUSTER SOFTWARE
Instrumentation
Telltales
Cameras
Video streaming
12

## Slide 13: Digital cockpit: Android guest
IVI
Hypervisor-enabled QNX microkernel (safety-certified)
Android guest
Cluster display
Vehicle data
virtio-input
virtual Bluetooth
Sensor data
virtio-net
virtio-video virtio-scmi
virtual camera etc.
virtio-gpu
virtio-snd
virtio-blk
virtio-vsock
CRITICAL IVI SOFTWARE
Cameras
Video streaming
Vehicle HAL
Graphics
Audio
System wide audio management
Touch events
Vehicle data
Audio
USB
Network
CRITICAL CLUSTER SOFTWARE
Instrumentation
Telltales
Cameras
Video streaming
13

## Slide 14: Digital cockpit: Optional Linux guest
14
IVI
Hypervisor-enabled QNX microkernel (safety-certified)
Android guest
virtio-input
virtual Bluetooth
Sensor data
virtio-net
virtio-video virtio-scmi
virtual camera etc.
Cluster display
Vehicle data
virtio-gpu
virtio-blk
virtio-net
virtio-vsock
virtio-scmi
Linux guest (optional)
virtio-gpu
virtio-snd
virtio-blk
virtio-vsock
CRITICAL IVI SOFTWARE
Cameras
Video streaming
Vehicle HAL
Graphics
Audio
System wide audio management
Touch events
Vehicle data
Audio
USB
Network
CRITICAL CLUSTER SOFTWARE
Instrumentation
Telltales
Cameras
Video streaming

## Slide 15: Rear Seat Entertainment: No Guests Running Yet
15
RSE2
Hypervisor-enabled QNX microkernel (safety-certified)
RSE1
Touch
Audio
USB
Network
CRITICAL RSE SOFTWARE
Video streaming
Graphics, audio, USB
Connected apps with controlled content
GLES/Vulkan apps
Media support
Audio management
Connections to cockpit

## Slide 16: Rear Seat Entertainment: Android Guests
RSE2
Hypervisor-enabled QNX microkernel (safety-certified)
RSE1
Android guest 2
virtio-gpu
virtio-blk
virtio-vsock
16
Android guest 1
virtio-input
virtual camera
virtio-snd
virtio-net
virtio-video
virtual Bluetooth
Touch
Audio
USB
Network
CRITICAL RSE SOFTWARE
Video streaming
Graphics, audio, USB
Connected apps with controlled content
GL ES/Vulkan apps
Media support
Audio management
Connections to cockpit
Videostreaming/YouTube™
Google Play™
Android browser and media processing
Multi-zone audio
Connections to cockpit

## Slide 17: A sample digital cockpit: Called “The Demonstrator”
Android Apps
Browser
Multimedia
Navigation
Camera
USB/WiFi/LTE
Bluetooth
Google Automotive Services
QNX Advanced Virtualization Frameworks
17
Instrument cluster
Infotainment and apps
QNX car critical software
QNX acoustics
QNX screen (graphics)
QNX Hypervisor
Digital cockpit hardware (ARMv8)

## Slide 18
18
© 2022 BlackBerry Limited. All Rights Reserved.
Technical Specifications

## Slide 19: Foundational Virtual Devices: Provided by the QNX Hypervisor
DEVICE/SERVICE | DESCRIPTION | HARDWARE PLATFORM | INDUSTRY VERSION/COMPATIBILITY
qvm: Virtual Machine | Virtual machine manager. Supports virtual CPUs and memory mappings for guest. | X86_64+ARMv8 | QNX
GICv2 | Interrupt controller | ARMv8 | ARM spec
GICv3 | Interrupt controller | ARMv8 | ARM spec
MC146818 | Realtime clock | X86_64 | Intel spec
8259 | X86 legacy PIC | X86_64 | Intel spec
HPET | High Precision Event Timer | X86_64 | Intel spec
IOAPIC | Intel Advanced PIC (interrupt controller) | X86_64 | Intel spec
PC_Keyboard | PC keyboard emulator (used for ctrl-alt-del) | X86_64 | Intel spec
PL011 | UART | ARMv8 | ARM spec
8250 | UART | X86_64+ARMv8 | Chip spec
Shared memory | Shared memory device | X86_64+ARMv8 | QNX
SMMU | System Memory Management Unit device for QNX guests | X86_64+ARMv8 | QNX. Requires host SMMU service (X86 or ARM)
8254 | Timers | X86_64 | Intel spec
VIRTIO block | Block device used for filesystem access | X86_64+ARMv8 | VIRTIO 1.2 including packed virtqueues
Qualcomm ICE | In-line Cryptographic Engine for block access | ARMv8 | Qualcomm
VIRTIO net | Network device | X86_64+ARMv8 | VIRTIO 1.2 including packed virtqueues
VIRTIO console | Console device used to buffer streaming devices | X86_64+ARMv8 | VIRTIO 1.2
SP805 | Watchdog device | ARMv8 | Chip spec
IB700 | Watchdog device | X86_64 | Chip spec
PCI | PCI support for guest | X86_64+ARMv8 | Chip spec
Entropy (RNG) | Random Number Generator | X86_64+ARMv8 | VIRTIO 1.2
Debug/progress virtual device | Debugging device / virtual machine execution progress | X86_64+ARMv8 | QNX
Tracing virtual device | Tracing device for debugging | X86_64+ARMv8 | QNX
Host to guest networking | Network device for QNX hypervisor host | X86_64+ARMv8 | VIRTIO 1.2
19

## Slide 20: QNX® Advanced Virtualization
QNX ADVANCED VIRTUALIZATION FRAMEWORKS (ANDROID)
Linux guests supported separately
SHARED GPU AND DISPLAY | VIRTIO 1.2.5.7 GPU DEVICE
Shared surface | Extends ‘Shared VPU and Display” to allow Android guest to display in QNX host
Virtual socket | VIRTIO 1.2.5.10 socket device
Shared input | VIRTIO 1.2.5.8 input device
Shared audio | VIRTIO 1.2.5.14 sound device – Includes System Wide Audio Management service (SWAM)
Shared video and camera | Supports ‘virtio-video’ as defined by latest technical committee draft. This specification is not yet approved
Shared USB | No standard exists. Allows allocation and use of USB devices by guest OS or hypervisor host
Sensor sharing | No standard exists. ‘virtio-scmi’ is proposed. Allows abstraction of a select set of Android HAL devices back to applications running the QNX host (e.g. Inertia Management Unit)
Shared filesystem | No official standard exists. Community standard only. ‘Virtio-fs’ is proposed. Allows guests to share the same host-based filesystem for read/write access using FUSE
QNX guest graphics sharing | No standard exists. Allows a QNX guest to render to a display controlled by the hypervisor host using virtio-gpu
Virtual Bluetooth | No standard exists. Virtualization of Bluetooth device from Android to hypervisor host
20

## Slide 21: Developing with graphics
Vulkan 1.2
VK_QNX_screen_surface
OpenGL ES 2D/3D
OpenGL ES, Vulkan programming in QNX Host and Android/Linux guest and cloud is moving towards a common build environment with no hardware specifics
QNX graphic applications
Graphics driver
Host: QNX Microkernel
Virtual machine
QNX graphic applications
Virtual machine
Hypervisor host
21
QNX guest microkernel
Virtual graphics/ SwiftShader
Android/Linux graphic applications
Guest kernel
SurfaceFlinger, GfxStream, Virgl, ANGLE, SwitchShader
virtio-gpu
virtio-gpu
OpenGL is a registered trademark and the OpenGL ES logo is a trademark of Hewlett Packard Enterprise used by permission by Khronos.
Vulkan and the Vulkan logo are registered trademarks of the Khronos Group Inc.
The Android robot is reproduced or modified from work created and shared by Google and used according to terms described in the Creative Commons 3.0 Attribution License.

## Slide 22: Example Virtual Device: Abstraction and Sharing of Audio: virtio-snd
22
QNX Hypervisor host
Android hypervisor guest
Apps
AudioFlinger
AudioHAL
TinyALSA
Linux Kernel
Linux hypervisor guest
Apps
ALSA
Linux Kernel
virtio sound driver
QNX hypervisor guest
Apps
Audio Resource Manager (io-audio)
virtio sound driver
QVM
virtio sound vdev
QVM
virtio sound vdev
QVM
virtio sound vdev
virtio deva driver
virtqueues/shared mem
virtqueues/shared mem
virtqueues/shared mem
hw deva drivers
Audio resource manager (io-audio)
virtio-snd
Multiple audio playback and capture channels presented to guests
Software mixers in host that can combine audio playback from guests and host
Software splitters
Supports Class 1, 2 and 3 audio for guest (one to one, transient and many to one)
Supports Audio Control HAL for Android (emit emergency chimes outside of Android)

## Slide 23: How QNX team can help
Guest environment
Custom kernel modules
Virtual machine environment
QNX Hypervisor host environment
Custom
front ends
AND
1
Custom applications | Guest drivers/stacks
2
3
Custom
back ends
4
Custom services
5
23
EXAMPLE 1 vehicle_server program provides vehicle data to apps running in guest
EXAMPLE 2 A custom front end is developed to exchange vehicle data with drivers in backend as an extension to VIRTIO. May involve kernel module.

## Slide 24: Futures
24
QNX ACTIVE IN SERIES TO EXTEND VIRTIO
Encoding of video
System-wide audio management
WORKING WITH HARDWARE PARTNERS ON NEXT GENERATION SOFTWARE DESIGN
E.g., Qualcomm GEN4 (82XX and others)
CONTINUING TO ADD TO OUR SAFETY-CERTIFIED PORTFOLIO WITH VIRTUAL DEVICES AND SUPPORTING BACKEND SOFTWARE
E.g., using safety-certified filesystems with safety-certified virtio device
Updates to Android (13) and Google Trout Configuration (1.1/1.2)
Linux 5.X kernels
Working with security teams to ensure we are meeting future requirements

## Slide 25: Thank you
25